SENSUM QGis-R tools v.
# Introduction
The Qgis-R tools are a collection of Quantum GIS (QGIS) scripts and models developed within the FP-7 SENSUM Project to implement algorithms for generating Focus Maps, a key step in the development of efficient data collection schemes. The tools are subdivided in scripts and models, each type referring to a specific scripting type (See QGIS Sextante documentation for further details). Each script is an ascii file containing an header and a body. The header contains a set of special instructions to automatically generate the graphical user interface of the script itself. The body of the script in this case is composed by R code. The scripts can acts as simple wrappers for R package and function, or can implement themselves original algorithms.
The models refer to a graphical processing environment recently introduced in QGIS. This framework allows for combining different algorithms, possibly developed themselves in different environments (R, GRASS, SAGA, OTB, etc) in a single processing pipeline which is defined by visual blocks (either inputs, or algorithms). Contrary to the scripts, the models are saved in a non-friendly ascii format and cannot be directly edited.
In the following a brief description of the tools and models implemented within the SENSUM project
# Installation
The scripts and models can be downloaded from https://www.github.com/SENSUM-Project/Qgis-R where the latest development version is residing.
Linux: copy all the files from the folder “rscripts” to the folder “~/.qgis2/processing/rscripts”. Copy all the files from the folder “models” to the folder “~/.qgis2/processing/models”. The files with extension “.help” contain a short documentation about the individual scripts/models.
Windows: same procedure, with the related paths (always in the user´s Documents folder).
The processing scripts are available in QGIS under the Processing->Toolbox menu item, which provides a simple graphical interface. When starting QGIS, all available scripts and models are automatically loaded.
In order to run the scripts, a clean R installation (<= 3.0) has to be present in the system.
# Scripts
## GenerateDensity
The script generates a two-dimensional density from a set of points (vector layer), using a kernel density approach.
### Inputs
vec_layer		Input vector layer contatining a set of points
sigma		Parameter of the kernel used to compute the density
resolution_x		X resolution of output raster
resolution_y		Y resolution of output raster

### Outputs
dens	raster	Output raster density

## GenerateFocusMap
The scripts takes in input a list of raster layers, and combines them to generate a Focus Map. Up to four input rasters can be used. Two different pooling can be chosen, either “linear” or “loglinear”. The normalization is based on a rejection bound approach for outliers rejection (a rejection bound [0,1] is equivalent to standard normalization). In case the input layers have different resolution and origin, they can be resampled (according to the first element of the list).
### Inputs
input_rasters	Multiple rasters	List of input raster layers, with same projection.
high_rejection_bound	number	Higher rejection bound (hrb). 0<=lrb<hrb<=1
low_rejection_bound	number	Lower rejection bound (lrb). 0<=lrb<hrb<=1
pooling_str	string	“linear” (additive) or “loglinear” (multiplicative)
resample_rasters	boolean	If “True” input rasters are resampled according to the first layer´s resolution
equal_weighting	boolean	If “True” weights are set equal to 1/n_input_layers
weight_1	number	Weight of first raster layer
weight_2	number	Weight of first raster layer
weight_3	number	Weight of first raster layer
weight_4	number	Weight of first raster layer

### Outputs
focus_map	Raster	Output raster layer. The extent is the intersection of the input layers´ extents

## GenerateFocusMap_2inputs
Same functionalities as GenerateFocusMap script, but with two fixed input raster layers to allow for graphical modeling.
### Inputs
input_raster1	raster	First input raster layer
input_raster2	raster	First input raster layer
high_rejection_bound	number	Higher rejection bound (hrb). 0<=lrb<hrb<=1
low_rejection_bound	number	Lower rejection bound (lrb). 0<=lrb<hrb<=1
pooling_str	string	“linear” (additive) or “loglinear” (multiplicative)
resample_rasters	boolean	If “True” input rasters are resampled according to the first layer´s resolution
equal_weighting	boolean	If “True” weights are set equal to 1/n_input_layers
weight_1	number	Weight of first raster layer
weight_2	number	Weight of first raster layer

### Outputs
focus_map	raster	Output raster layer. The extent is the intersection of the input layers´ extents

## RasterFlip_y
Performs a flipping of the input raster around 'y' axis.
### Inputs
raster_layer	raster	Input raster layer

### Outputs
output_layer	raster	Output raster layer

# Models
## Demo_cologne_1
### Inputs

### Outputs